## Slide 1
Autonomous Vehicle Assignment and Routing in Congested Networks
Jiangtao Liu (jliu215@asu.edu)
Xuesong Zhou (xzhou74@asu.edu)
School of Sustainable Engineering and the Built Environment
Pitu Mirchandani (pitu@asu.edu)
School of Computing, Informatics, and Decision Systems Engineering (CIDSE)
Arizona State University
T3 Webinars are sponsored by ITS Professional Capacity Building Program, ITS Joint Program Office,
U.S. Department of Transportation

## Slide 2
  2. Problem Statement
  3. Space-Time-State Network Flow Models
  4. Dantzig-Wolfe Decomposition Algorithm
Outline
  5. Preliminary Experiments
  1. Introduction
  6. Summary

## Slide 3
1. Introduction
Ride Sharing Companies
Information-sharing technology

## Slide 4
The “three revolutions” in the future transportation systems
1. Introduction

## Slide 5
Picture source: McKinsey&Company, 2016. An integrated perspective on the future of mobility.
Future urban transportation systems: integrated multi-modal scheduled transportation system
1. Introduction

## Slide 6
Vehicle Supply
Trip Demand
Vehicle-to-passenger assignment
Capacity：
Road/transit line/Signal/Depot/Parking
Routing and Congestion
Infrastructure Design
How to optimize demand, supply and infrastructure?
Pickup/drop-off location
Time windows
Origin/destination
1. Introduction

## Slide 7
Key questions:
How many autonomous vehicles do we need?
How many passengers can we serve?
How to capture the new traffic congestion?
What is the best vehicle routing and vehicle-to-passenger assignment solution?
1. Introduction

## Slide 8
Traffic Assignment Problem:
Network: Physical traffic network
Objective function: System Optimal or User Equilibrium
Road capacity: considered to capture road congestions
Vehicle-to-passenger assignment: given in advance
Passenger trip request: has the same origin and destination as that of the assigned vehicles
Vehicle carrying capacity: not explicitly considered
Variable: usually continuous vehicle flow
2. Problem Statement

## Slide 9
Vehicle Routing Problem:
Network: Virtual point-to-point network
Objective function: System Optimal
Traffic congestion: not explicitly considered
Vehicle-to-passenger assignment: will be found
Passenger trip request: has specific pick-up and drop-off location with time windows
Vehicle carrying capacity: considered
Variable: discrete vehicle routing and scheduling
2. Problem Statement

## Slide 10
Keywords:
Physical traffic network to consider traffic congestion
Trip requests with Pickup and delivery with time windows
Autonomous vehicles with carrying capacity for ride sharing
Central control (System optimal)
2. Problem Statement

## Slide 11
Link Capacity
Without link capacity:
Total cost is 6
With link capacity:
Total cost is 15
2. Problem Statement

## Slide 12
System Optimal Coordination
Without coordination (selfish routing):
Total cost is 15
With coordination:
Total cost is 9
2. Problem Statement

## Slide 13
Time windows
The red vehicle can wait until time 3 to pick up passenger 2, so the blue vehicle can pick up passenger 1 at exact time 3.
The optimal result doesn’t only optimize the vehicle routing, but also the departure time of picked up passengers.
Total cost is 9
2. Problem Statement

## Slide 14
Ridesharing (vehicle carrying capacity)
When the red vehicle’s carrying capacity is increased to 2, the total cost is reduced to 4 from 9;
Only the red vehicle is required to serve the trip requests.
Total cost is 4
2. Problem Statement

## Slide 15
The Challenge of solving system optimal vehicle routing with pickup and drop-off location and time windows in congested physical traffic networks:
System-impact of adjusting one vehicle routing:
System marginal vehicle travel cost
System marginal passenger service benefit/cost
[Time window]
[Time window]
In this queuing system:
Waiting time for individual: 4 min
After adding one more person in the queue:
Societal travel time: additional 4 min for each person behind: +16 min, and the waiting time of added person is 4 min, so the system marginal waiting time is 20 min.
Societal service benefit: some persons may not be served in their preferred time window and it decreases the service benefit.
2. Problem Statement

## Slide 16
Marginal cost calculation in system optimal dynamic traffic assignment (SODTA)
Ghali and Smith (1995)
Ghali, M.O. and Smith, M.J., 1995. A model for the dynamic system optimum traffic assignment problem. Transportation Research Part B: Methodological, 29(3), pp.155-170.
2. Problem Statement

## Slide 17
Our Approach 1: Marginal Cost Calculation
Step 1: Build virtual pickup and drop-off links in physical traffic networks, and its service pricing is converted to generalized link travel cost
Step 2: find one initial solution as the input
Step 3: Perform network loading within a space-time-state network
  3.1 use cumulative arrival and departure counts to derive the link marginal travel cost.
  3.2 update the marginal service link benefit of passengers (not served or served by multiple vehicles)
Step 4: find the new least-marginal-cost route for each vehicles, and go to step 3; otherwise, stop.
2. Problem Statement

## Slide 18
Our Approach 2: Dantzig-Wolfe Decomposition
Restricted master problem
Road capacity constraint
Passenger service constraint
Subproblems
(Time-dependent State dependent shortest path problem for each vehicle)
Marginal costs from the solver
Vehicle routing solution
Solved by standard solvers
Solved by the beam-search algorithm in space-time-state networks
2. Problem Statement

## Slide 19
3. Space-time-state network and model formulation
Add virtual pick-up and drop-off nodes and links for each passenger

## Slide 20
Time-extended Space-time network construction for physical path
Arc (i,j,t,s) with capacity
Vertex (i,t), (j,s)
Passenger pickup and drop-off time windows and locations are embedded in this network
3. Space-time-state network and model formulation
Space-time network

## Slide 21
Challenge: how to model the logit of passenger pickup and delivery with vehicle carrying capacity
One more dimension-> Vehicle Carrying States:
which passengers are being carried by this vehicle:
  To record the passenger service status:
  0: the passenger is not served;
    1: under served (picked up but not delivered);
    2: finished (delivered)
Example: In the case: if vehicle capacity is 1 and 2 passengers trip requests,
All possible states: [ ], [1[1]], [1[2]], [2[1]] or [2[2]]
3. Space-time-state network and model formulation

## Slide 22
Vehicle carrying state transition logit: focusing on specific passenger 1
0->0: vehicle departs at the origin depot
0->1[1]: passenger 1 is picked up at his location within time window.
1[1]->1[2]: passenger 1 is dropped off at his location within time window
1[2]->0: vehicle arrives at the destination depot.
Once one passenger is picked up, he/she will always be dropped off, because 1[1]->0 is not a feasible state transition.
No passenger will be served if the vehicle carrying capacity is fully used.
3. Space-time-state network and model formulation

## Slide 23
Vehicle State Transition with specific locations and time intervals
Vehicle carrying state transition graph
3. Space-time-state network and model formulation

## Slide 24
One possible vehicle trajectory in a space-time-state network
Vertex:
Arc:
space
state
3. Space-time-state network and model formulation
time

## Slide 25
Mathematical formulation:
(1)
(1) Flow balance constraint for each vehicle:
(2)
(2) Passenger pick-up request at :
(3)
(3) Tight road capacity constraint (point queue model)
(4)
(4) Binary variables
(5)
3. Space-time-state network and model formulation

## Slide 26
Capture queue spillback:
Inflow arc capacity constraint:
(6)
Outflow arc capacity constraint:
(7)
Link storage capacity constraint:
(8)
Newell’s simplified kinematic wave model (Newell, 1993)
(9)
3. Space-time-state network and model formulation

## Slide 27
4. Dantzig-Wolfe Decomposition Algorithm
Special block: time-dependent state-dependent shortest path problem
Objective function
A special block can be solved by our VRP solution engine
can be the subproblem in Dantzig-Wolfe decomposition

## Slide 28
Restricted master problem
Pick-up constraint:
Capacity constraint:
Column selection:
4. Dantzig-Wolfe Decomposition Algorithm

## Slide 29
Subproblems (TDSDSP)
Dual variable/ marginal cost of passenger pickup constraints
Dual variable/ marginal cost of congestion constraints
Dual variable/ marginal cost of path weight constraints
4. Dantzig-Wolfe Decomposition Algorithm

## Slide 30
4. Dantzig-Wolfe Decomposition Algorithm

## Slide 31
A tree-based path representation
One-to-all shortest path tree is generated for one vehicle
Directly obtain the shortest path for vehicles with a same depot and departure time but different destination depot
Does not need to run the shortest path algorithm again to improve the computation efficiency.
A tree-based path representation
4. Dantzig-Wolfe Decomposition Algorithm

## Slide 32
Sioux Falls Network
# of nodes | 24
# of links | 84
# of trip requests (pickup and drop-off with time windows) | 30
# of available autonomous vehicles | 30
# of depots | 5
optimization time horizon (time unit) | 110
Vehicle capacity (person) | 1
5. Preliminary Experiments

## Slide 33
Vehicle_No | Passenger_No | Vehicle_No | Passenger_No | Vehicle_No | Passenger_No
1 | [15] | 11 | [20] | 21 | [23]
2 | [8] | 12 | [26] | 22 | [25]
3 | [1] | 13 | [16] | 23 | [22]
4 | [7] | 14 | [18] | 24 | [19]
5 | [9] | 15 | [2] | 25 | [4]
6 | [11] | 16 | [10] | 26 | [5]
7 | [29] | 17 | [3] | 27 | [24]
8 | [28] | 18 | [12] | 28 | [14]
9 | [17] | 19 | [27] | 29 | [13]
10 | [21] | 20 | [30] | 30 | [6]
Initial feasible solution
5. Preliminary Experiments

## Slide 34
Dantzig-Wolfe decomposition algorithm solution:
 | Number of required vehicles | Total travel cost
Initial solution | 30 | 1096
vehicle carrying capacity is 1 | 27 | 967.5
vehicle carrying capacity is 2 | 25 | 869.5
Each passenger has specific pickup and drop-off location and time windows
The vehicle benefit of serving one passenger is 20
The vehicle waiting cost is the half of the waiting time
Take vehicle 9 as an example:
In initial solution: picks up passenger 17 -> drops off passenger 17;
Vehicle carrying capacity is 1: picks up passenger 17 -> drops off passenger 17-> picks up passenger 29 -> drops off passenger 29
Vehicle carrying capacity is 2: picks up passenger 17 -> drops off passenger 17-> picks up passenger 30-> picks up passenger 29-> drops off passenger 29-> drops off passenger 30
5. Preliminary Experiments

## Slide 35
6. Summary
Our goals:
Minimize the system-level travel cost, including vehicle travel time and service benefits
Satisfy passengers’ trip requests with pickup and drop-off location and time windows
Consider the road congestion incurred by assigned vehicles
Future Extension: multi-modal scheduled transportation system: human-driven vehicles, autonomous vehicles, and public transit systems.

## Slide 36
Dantzig-Wolfe decomposition algorithm
Space-time-state network construction and network flow model
Required knowledge:
Dynamic Traffic Assignment and Vehicle Routing Problem
Time-dependent State-dependent shortest path problem
6. Summary

## Slide 37
References
Space-time-state network flow models and vehicle routing problem:
  1. Mahmoudi, M. and Zhou, X., 2016. Finding optimal solutions for vehicle routing problem with pickup and delivery services with time windows: A dynamic programming approach based on state–space–time network representations. Transportation Research Part B: Methodological, 89, 19-42.
  2. Liu, J., Kang, J., Zhou, X., Pendyala, R., 2018. Network-oriented household activity pattern problem for system optimization. Transportation Research Part C 94, 250-269
  3. Zhou, X., Tong, L., Mahmoudi, M., Zhuge, L., Yao, Y., Zhang, Y., Shang, P., Liu, J. and Shi, T., 2018. Open-source VRPLite Package for Vehicle Routing with Pickup and Delivery: A Path Finding Engine for Scheduled Transportation Systems. Urban Rail Transit, 4(2), 68-85.
Dynamic Traffic Assignment and Traffic flow model:
  4. Lu, C.C., Liu, J., Qu, Y., Peeta, S., Rouphail, N.M. and Zhou, X., 2016. Eco-system optimal time-dependent flow assignment in a congested network. Transportation Research Part B: Methodological, 94, pp.217-239.
  5. Zhou, X. and Taylor, J., 2014. DTALite: A queue-based mesoscopic traffic simulator for fast model evaluation and calibration. Cogent Engineering, 1(1), p.961345.
Dantzig-Wolfe Decomposition algorithm
  6. https://en.wikipedia.org/wiki/Dantzig%E2%80%93Wolfe_decomposition